Geometry 3
I.Hrivnacova
IPN, Orsay
Most slides thanks to M. Asai, SLAC
Cours Geant4 @ Paris 2007
4 - 8 June 2007

---
Contents
Geometry checking tools
Basics of Touchable
Region

---
Contents
Geometry checking tools
Basics of Touchable
Region

---
Malformed Geometries
A protruding volume is a contained daughter volume which actually protrudes from its mother volume.
Volumes are also often positioned in a same volume with the intent of not provoking intersections between themselves. When volumes in a common mother actually intersect themselves are defined as overlapping.
Geant4 does not allow for malformed geometries, neither protruding nor overlapping.
  - The behavior of navigation is unpredictable for such cases.
overlapping
protruding

---
Debugging Geometries
The problem of detecting overlaps between volumes is bounded by the complexity of the solid models description.
Utilities are provided for detecting wrong positioning
  - Optional checks at construction
  - Kernel run-time commands
  - Graphical tools (DAVID, OLAP)

---
Debugging Geometries
Optional checks at construction
Constructors of G4PVPlacement and G4PVParameterised have an optional argument “pSurfChk”:
  - G4PVPlacement(G4RotationMatrix* pRot, ..., ,
            G4bool pSurfChk=false);
If this flag is true, overlap check is done at the construction.
  - Some number of points are randomly sampled on the surface of creating volume.
  - Each of these points are examined
    - If it is outside of the mother volume, or
    - If it is inside of already existing other volumes in the same mother volume.
  - This check requires lots of CPU time, but it is worth to try at least once when you implement your geometry of some complexity.

---
Debugging Geometries
Debugging run-time commands
Built-in run-time commands to activate verification tests for the user geometry:
To start verification of geometry for overlapping regions based on a standard grid setup, limited to the first depth level:
  - geometry/test/run or geometry/test/grid_test
To apply the grid test to all depth levels (may require lots of CPU time!)
  - geometry/test/recursive_test
To shoot lines according to a cylindrical pattern
  - geometry/test/cylinder_test
To shoot a line along a specified direction and position
  - geometry/test/line_test
To specify position for the line_test
  - geometry/test/position
To specify direction for the line_test
  - geometry/test/direction

---
Debugging Geometries
Debugging run-time commands
Example of output:
GeomTest: no daughter volume extending outside mother detected.
GeomTest Error: Overlapping daughter volumes
The volumes Tracker[0] and Overlap[0],
both daughters of volume World[0],
appear to overlap at the following points in global coordinates: (list truncated)
length (cm) ----- start position (cm) ----- ----- end position (cm) -----
240 -240 -145.5 -145.5 0 -145.5 -145.5
Which in the mother coordinate system are:
length (cm) ----- start position (cm) ----- ----- end position (cm) -----
. . .
Which in the coordinate system of Tracker[0] are:
length (cm) ----- start position (cm) ----- ----- end position (cm) -----
. . .
Which in the coordinate system of Overlap[0] are:
length (cm) ----- start position (cm) ----- ----- end position (cm) -----

---
Debugging Geometries
DAVID
DAVID is a graphical debugging tool for detecting potential intersections of volumes
Accuracy of the graphical representation can be tuned to the exact geometrical description.
  - Physical-volume surfaces are automatically decomposed into 3D polygons
  - Intersections of the generated polygons are parsed.
  - If a polygon intersects with another one, the physical volumes associated to these polygons are highlighted in color (red is the default).
DAVID can be downloaded from the Web as external tool for Geant4
  - http://geant4.kek.jp/~tanaka

---
Debugging Geometries
OLAP
Stand-alone batch application
  - Provided as extended example; Can be combined with a graphical environment and GUI

---
Debugging Geometries
Visualizing detector geometry tree
Built-in commands defined to display the hierarchical geometry tree
  - As simple ASCII text structure
  - Graphical through GUI (combined with GAG)
  - As XML exportable format
Implemented in the visualization module as an additional graphics driver
Provide G3 DTREE capabilities and more

---
Contents
Geometry checking tools
Basics of Touchable
Region

---
Basics Of Touchables
Suppose a geometry is made of sensitive layers C which are placed in a volume B
Volume B is a daughter volume of a divided volume A
B
B
C
A
The volume A has a 24 positions in the world
While in the 'logical' geometry tree the volume C is represented by just one physical volume, in the real world there are many C 'volumes'
How can we then identify these volumes C ?

---
Basics of Touchables
A touchable for a volume serves the purpose of providing a unique identification for a detector element
It is a geometrical entity (volume or solid) which has a unique placement in a detector description
  - It can be uniquely identified by providing the copy numbers for all daughters in the geometry hierarchy
  - In our case these are
    - CopyNo of C in B: 1
    - CopyNo of B in A: 1,2,3
    - CopyNo of A in the world: 1, .., 24
  - Example of touchable identification:
    - A.3/B.2/C.1
B.1
B.2
B.3
C.1
A.1
A.2
A.3
...
A.4

---
Basics of Touchables
G4VTouchable
G4VTouchable - a base class for all touchable implementations – defines the following 'requests' (methods) which all touchable have to respond, where depth means always the number of levels up in the tree to be considered:
  - depth = 0 : the bottom level (volume C in B)
  - depth = 1 : the level of its mother volume (volume B in A)
  - depth = 2 : the grandmother volume (volume A in world)
GetCopyNumber(G4int depth =0)
  - returns the copy number of the given level
GetTranslation(G4int depth = 0)
GetRotation(G4int depth=0)
  - return the components of the volume's transformation
GetSolid(G4int depth =0)
  - returns the solid
GetVolume(G4int depth =0)
  - returns the physical volume

---
Basics of Touchables
Accessing touchable in Tracking
Full geometrical information available via touchable
  - to processes, to user code: sensitive detectors, hits
During tracking, the current touchable can be accessed via G4Step object
  - MySteppingAction::UserSteppingAction(const G4Step* step)
  - {
  - // Get touchable from step
  - const G4VTouchable* touchable
= step->GetPreStepPoint()->GetTouchable();
  - // Get copy numbers
  - G4int copyNo_B = touchable->GetCopyNumber(1);
  - G4int copyNo_A = touchable->GetCopyNumber(2);
  - }
Use pre-step point rather than post-step point,
as when crossing geometry boundary the post-step
point belongs already to the next volume

---
Contents
Geometry checking tools
Basics of Touchable
Region

---
Region
A region is a part of the geometry hierarchy, i.e. a set of geometry volumes, typically of a sub-system.
  - A logical volume can be a region.
A region may hold its own user defined setting affecting tracking
  - It is useful in complex geometry setups, such as those found in large detectors in particle physics experiments, where different sub-systems may require different level of detail simulation
Please note :
World logical volume is recognized as the default region. User is not allowed to define a region to the world logical volume.

---
Region
Region Properties
A region may have its unique
  - Production thresholds (cuts)
  - User limits
    - Artificial limits affecting to the tracking, e.g. max step length, max number of steps, min kinetic energy left, etc.
    - You can set user limits directly to logical volume as well. If both logical volume and associated region have user limits, those of logical volume wins.
  - User region information
    - E.g. to implement a fast Boolean method to identify the nature of the region.
  - Fast simulation manager
  - Regional G4UserSteppingAction (a new feature in v 9.0)

---
Region
Root Logical Volume
A logical volume becomes a root logical volume once a region is assigned to it.
  - All daughter volumes belonging to the root logical volume share the same region, unless a daughter volume itself becomes to another root.
Important restriction :
  - No logical volume can be shared by more than one regions, regardless of root volume or not.
Root logical - Region A
Root logical - Region B

---
Region
G4Region
A region is instantiated and defined by
  - G4Region* aRegion = new G4Region(“region_name”);
  - aRegion->AddRootLogicalVolume(aLogicalVolume);
  - Region propagates down to all geometrical hierarchy until the bottom or another root logical volume.
The region can be accesed by its name via G4RegionStore:
G4Region* myRegion
= G4RegionStore::GetInstance()->GetRegion(“region_name”);

---
Region
G4Region
Production thresholds (cuts) can be assigned to a region in a user physics list
  - void MyPhysicsList::SetCuts()
  - {
  - // Default production thresholds for the world volume
  - SetCutsWithDefault();
  - // Production thresholds for detector regions
  - G4ProductionCuts* cuts = new G4ProductionCuts;
  - cuts->SetProductionCut(cutValue);
  - G4Region* region = G4RegionStore::GetInstance()
  - ->GetRegion(“myRegion”);
  - region->SetProductionCuts(cuts);
  - }